## Slide 1: Overcoming challenges with scale-up and GMP implementation of an integrated dynamic bioprocessing (IDB) platform for multiple products
ICB 2025
Nicole A. Bleckwenn, Ph.D.
Kate Harvey & MTD team, Jon Coffman, Carrington Edmunds, Ken Lee & BTE team, CCFS team, PPS team, Dan Pappas & MS team, QA team, and Operations and Regulatory Colleagues
On behalf of the entire AZ organization developing and supporting IDB implementation

## Slide 2: Agenda
Background - IDB platform
Implementation strategy
Scale-up and GMP implementation challenges and lessons learned
Future direction and a challenge to our industry

## Slide 3
Integrated Dynamic Bioprocessing (IDB) Platform
Virus Inactivation
Load Adjustment
Load Adjustment
Dual Column Affinity Capture
Dual Depth Filtration (Optional)
Dual Column FT-Polishing
Dual Column B&E-Polishing
Dual Virus Filtration
Asymmetric Dialysis
Variable Perfusion Bioreactor
Load Adjustment
Slide modified and courtesy of Nikunj Sharda and Jon Coffman

## Slide 4: Drivers of IDB GMP Implementation Strategy
Speed of the pipeline
Biopharma and V&I therapeutic areas can be more sensitive to margin than oncology or rare disease areas
Account for upside and downside risks
Limited initial capital
Plant capacity and CMO capability
Diverse product portfolio with wide ranging demand
Product quality (labile molecules)

## Slide 5
IDB Clinical GMP Manufacturing Implementation Plan*
2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035
Potential Clinical and Commercial Scale IDB Product Manufacturing Timelines Based on New Candidate Drug IDs (CDIDs)
Project 1 Ph3 Mfg
Project 2 Ph3 Mfg
Project 3 Ph3 Mfg
Project 5 Ph3 Mfg
Project 7 Ph3 Mfg
Project 8 Ph3 Mfg
Project 9 Ph3 Mfg
1st clinical plant online
5
Project 1 Mfg
Project 4 Mfg
Project 5 Mfg
Project 6 Mfg
Project 7 Mfg
2nd clinical plant online
Project 8 Mfg
Project 9 Mfg
Project 10 Mfg
Project 11 Mfg
Project 12 Mfg
Project 13 Mfg
Project 14 Mfg
CDIDs in IDB
CDIDs in Fed-Batch/Intensifed Fed-Batch
Engr Run 1st plant
* Project timelines estimated
Engr Run 2nd plant
Engr Run CMO plant
Phase 3 Production in Clinical Plant
Phase 3 Production in Clinical Plant or Commercial Plant/CMO
Phase 1/2 Production in Clinical Plant

## Slide 6: Strategic Planning for Scale-Up and GMP Production
Planning is key
Strategic alignment of technical and regulatory goals
Thorough technology evaluation
Maintaining GMP standards
Don’t forget to address the people element
Scale-up bioreactor & TFF
Our particular challenges
New technology
  Build new automation
Implementation in older traditional stainless fed-batch facility
Defining the “sterile” boundary much wider than previous experience
Dynamic nature
  Batch definition
  Response time strategy without 24/7 staffing
Balance robustness with flexibility

## Slide 7: Failure Modes During Scale-up: Some Old, Some New
Multiple contaminations of bioreactor
  More opportunity with:
    More connections
    Complex hand-built and autoclaved parts
    Wider “sterile boundary”
  Contamination of media/feed additions
Bubbles in “high” downstream product lines due to gas permeability of tubing
CM precipitation
Notes: Building the plane as you attempt to fly it
Scaling protocols from lab to pilot scale often reveals unexpected challenges related to equipment and process dynamics that must be addressed.
Maintaining process reproducibility while adhering to GMP standards is essential to build confidence for full-scale manufacturing.

## Slide 8: The People Element
Write it down early and share often
Can’t always do it the way we’ve done it
Failures are an opportunity to learn
Collaboration is key!

## Slide 9: Engineering Run in GMP Clinical Facility (Molecule A)
Purpose: Shake down equipment with an IDB process through the second polishing step
  Limited to 10 production bioreactor days due to time available in plant

## Slide 10: Upstream Engineering Run - Growth
Lower osmolality may impact peak VCD
Early lower osmolality observed due to cumulative effect of wide tolerances on concentrated media and water addition
Chart: VCD
| 0 | 0.9 | 1.93 | 2.91 | 4 | 4.99 | 5.93 | 6.92 | 7.9 | 8.91 | 9.92 | 11.01 | 12 | 12.9 | 13.9
B2953-D48 - 3L | 10.3 | 19.2 | 36.8 | 63.5 | 94.5 | 118.1 | 104.1 | 90.3 | 80.7 | 67.9 | 67.56 | 47.1 | 43 | 53.9 | 47.6
B2992 - 50L Stainless Steel | 11.1 | 18.6 | 34.3 | 75.2 | 103.6 | 112.1 | 116.5 | 77.9 | 74.3 | 75.92 | 60.88 | 53.3 | 47.8 | 48.8 | 36.4
B3314 - 500L GPF ABEC | 10.7 | 17.7 | 33.2 | 59.9 | 80.9 | 84.6 | 81.5 | 93.2 | 79.7 | 88.4 | 66.4
Engr Run Clinical Manufacturing
Bench
Pilot
Chart: Osmolality
| 0 | 0.9 | 1.93 | 2.91 | 4 | 4.99 | 5.93 | 6.92 | 7.9 | 8.91 | 9.92 | 11.01 | 12 | 12.9 | 13.9
B2953-D48 - 3L | 322 | 341 | 307 | 310 | 313 | 328 | 345 | 355 | 357 | 362 | 370 | 374 | 379 | 381 | 382
B2992 - 50L Stainless Steel | 312 | 292 | 310 | 318 | 323 | 336 | 347 | 326 | 340 | 334 | 343 | 350 | 376 | 367 | 389
B3314 - 500L GPF ABEC | 337 | 288 | 271 | 283 | 276 | 301 | 336 | 362 | 369 | 383 | 379

## Slide 11: Downstream Engineering Run - Capture Overlays
Elution UV
*Expected Elution CVs: ~ 3.0
Column A
Column B
Last cycle, limited material
First cycles of each column cut early due to imposed limit of 24 hour load time for bioburden control (when titer is lowest)

## Slide 12: Downstream Engineering Run – Impact of Filter Swap
Engineering run filter swap impacts CM concentration
Downstream capture dampens impact of filter swap during engineering run
Chart: CM Tank Titer
| 0.63541666666666663 | 0.8125 | 1.3180555555555555 | 1.5194444444444444 | 1.7194444444444446 | 2.3159722222222223 | 2.7381944444444444 | 3.3138888888888891 | 3.7291666666666665 | 4.3159722222222223 | 4.5534722222222221 | 4.865277777777778 | 5.3145833333333332 | 5.5465277777777775 | 5.8805555555555555 | 6.354166666666667 | 6.5645833333333332 | 6.8493055555555555 | 7.3104166666666668 | 7.5604166666666668 | 7.7062499999999998 | 7.7458333333333336 | 7.8041666666666671 | 7.8361111111111112 | 7.8784722222222223 | 8.3152777777777782 | 8.5472222222222225 | 8.7645833333333343 | 8.8472222222222214 | 9.4034722222222218 | 10.39861111111111
WL8074 | 0.07 | 0.08 | 0.12 | 0.14 | 0.16 | 0.25 | 0.34 | 0.45 | 0.59 | 0.76 | 0.81 | 0.86 | 0.9 | 0.91 | 0.95 | 0.99 | 1.07 | 1.11 | 1.11 | 1.14 | 1.18 | 1.28 | 1.77 | 1.96 | 2.1 | 2.26 | 2.09 | 1.97 | 1.95 | 1.87 | 1.72
BTE 3L Data | 0.11 | 0.15333 | 0.25 | 0.43667 | 0.74 | 0.96333 | 1.1267 | 1.4467 | 1.4167 | 1.5767 | 1.8233 | 1.6933 | 2.0067 | 1.8933 | 1.9433
SUL Run #1 | 0.08 | 0.138 | 0.32 | 0.616 | 1.107 | 1.494 | 1.633 | 1.388 | 1.285 | 1.291 | 1.312 | 1.327 | 1.313 | 1.368 | 1.364
Chart: Engr Run Concentration by SOLO_A280
| 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
ProA Product | 16.8847 | 16.9729 | 16.7998 | 16.8168 | 16.7896 | 16.2626 | 16.2798 | 16.3187
AEX Product | 12.8572 | 12.8733 | 12.9681 | 12.9401 | 12.9042
CEX Product | 16.7522
Engr Run Clinical Manufacturing
Bench
Pilot
TFF Filter Swap

## Slide 13: First GMP Campaign – Molecule B (labile molecule)
Continuous through affinity capture only
3rd TFF filter swap failure likely caused by “less synchronized” manual valve switching
  Long term mitigation: automated filter swaps (in scale-up demonstration currently)
Drug Substance successfully released!
Dual Column Affinity Capture
Perfusion Bioreactor
Affinity Pool
Remainder batch operation

## Slide 14: And then we switched from some “easy” molecules to a “difficult” molecule (Molecule C)…

## Slide 15: TFF Scaling Concerns
Next product (Molecule C):
  Fouling mechanism changed- included product binding
  14 filters required for clinical manufacturing under platform conditions
    Excessive number of outlet/inlet ports on BRX bag
    Large footprint required
    Numerous retentate/permeate pumps
    High demand on operators
Slide modified and courtesy of Ana Dilillo

## Slide 16
Part of the Solution: TFF Regeneration
The highest cost consumables in the IDB process are TFF membranes ​
Directionally, cell culture and titer continue to increase resulting in greater filter area demand
TFF Regeneration is a process to remove foulants from the membrane without stopping perfusion
TFF Regeneration employs swapping between two sets of TFFs, so that one set is always operating perfusion, while the second set is being cleaned and equilibrated
TFF Regeneration will reduce the required filter area and improve facility fit design
Slide modified and courtesy of Ana Dilillo

## Slide 17
Chart: Elapsed Culture Time (Days)
| 0.03 | 0.86 | 1.83 | 2.89 | 3.99 | 4.91 | 5.85 | 6.93 | 7.83 | 8.84 | 9.85 | 10.93 | 11.86 | 12.92 | 13.84
Bench Scale 1x Flux | 102.18 | 98.98 | 85.9 | 91.1 | 89.6 | 89 | 84.15 | 76.12 | 72.8 | 64.41 | 60.24 | 47.42 | 37.89 | 43.37 | 41.63
Bench Scale 3-4x Flux | 97.0579 | 86.8803 | 90.2225 | 95.1444 | 90.1821 | 84.9092 | 80.7717 | 70.6885 | 63.0753 | 48.9938 | 40.2571 | 44.6622 | 25.0355 | 17.5587 | 8.0614
Large Bench 3-4x Flux | 266.6667 | 75 | 100 | 88.8889 | 84.6154 | 77.0833 | 64.2857 | 58.3333 | 63.4615 | 50.8197 | 41.6667 | 33.945 | 28.125 | 26.1438 | 21.5962
Large Bench 3-4x Flux w/ Regeneration | 100 | 72.7273 | 88.8889 | 89.4737 | 78.5714 | 66.3934 | 59.2593 | 55.2448 | 88.7324 | 89.5105 | 89.5105 | 85.4167 | 82.7586 | 61.7647 | 59.1549 | 53.012 | 83.8323 | 82.5301 | 80.1205 | 77.7108 | 76.3636 | 70.2381 | 49.7143 | 42.5641 | 38.806 | 78.866 | 78.866 | 74.7423 | 71.6495 | 70.1031 | 64.433 | 45.6522
TFF Regeneration Performance Reduces Filter Demand
TFF Regeneration swaps performed on days 7, 10, and 13
Combination of higher flux with TFF regeneration resulted in 2-3 fold filter demand
  Projected 4-8 TFF filters vs 14 for clinical manufacturing
No impact to cell culture performance
No impact to product quality
89%
84%
79%
TFF1
TFF2
TFF1
TFF2
Pilot 3-4x Flux with Regeneration
Bench 1x Flux
Pilot 3-4x Flux
Bench 3-4x Flux
Slide courtesy of Ana Dilillo

## Slide 18
Single Pass Operation
Cycling Operation
Polish Step 1
Affinity Capture product vessel
22 filters required
Titrant
Polish Buffer(s)
Cumulative 75 L Hold-up volume
Next Issue: Molecule C forms precipitate when load adjusting prior to first polishing step
Polish Step 1
Depth Filter FT + Chase vessel
4 filters required
Affinity Capture product vessel
Titrant
7 L Hold-up volume
Filter Sani Buffer(s)
Polish Buffer(s)
Precipitate forms
300-500 NTU
Slide courtesy of David Sherr

## Slide 19
Slide courtesy of David Sherr
Single Pass Operation
Cycling Operation
Polish Step 1
Affinity Capture product vessel
22 filters required
Titrant
Polish Buffer(s)
Cumulative 75 L Hold-up volume
Mitigation: Continuous depth filter cycling reduces filter demand/hold-up volume and allows for bioburden control
Polish Step 1
Depth Filter FT + Chase vessel
4 filters required
Affinity Capture product vessel
Titrant
7 L Hold-up volume
Filter Sani Buffer(s)
Polish Buffer(s)
Precipitate forms
300-500 NTU

## Slide 20: The Journey Forward
Continuous evolution and improvement
TFF regeneration and depth filter cycling are in scale-up testing now
Next GMP campaign will include these and process through 2nd polishing step
Future scale-up work and GMP campaigns will incorporate viral filtration and asymmetric dialysis
Feedback to the IDB platform team will refine and improve the process
A challenge to us all
Push the limits of traditional paradigms
  explore new technologies
  set ambitious targets
  collaborate to redefine bioprocessing boundaries
Emerging technologies and digital tools offer opportunities to increase automation and enhance data-driven decision-making in continuous biomanufacturing

## Slide 21: Thank you