## Slide 1: Leveraging Scale-down Methods to Accelerate Harvest Characterization
A.A. Joseph, M. Mollet & J. Bender
2016 Harvest Industry Summit
Company Restricted
3rd-5th May 2016

## Slide 2: Introduction
Pilot-scale centrifuge is typically utilized to model commercial-scale systems
  Large material & resource requirement
  Testable parameters limited & narrow data set obtained
Objective to develop a scale-down model to improve efficiency
Scale-Down model benefits:
  High throughput → can test more conditions
  Ability to use material from bench-scale bioreactors
  At least $13,000 cost savings in raw materials per study
Material evaluated to confirm comparable shear and particle characteristics
Established bench-scale conditions to model Alfa-Laval LAPX-404 & BTPX-305

## Slide 3: USD Centrifugation: Approach
3
Bioreactor
Disk-Stack Centrifuge
EDR
Shear Device
Lab-Scale
Centrifuge
Scale-Down Model
Pilot-Scale Centrifugation
Attribute | LDH | Calculated EDR | Turbidity | PSD | Filterability
Theoretical Shear |  |  |  |  | 
Degree of Cell Damage |  |  |  |  | 
Particle Characteristics |  |  |  |  | 

## Slide 4: USD Centrifugation: Separation
Centrifugation performance typically described using the Sigma concept of equivalent settling area
Q/Σ commonly used as a basis for scale-up of continuous centrifugation
Centrifuges of different sizes and designs can be compared using the equation below
  Correction factor “c” allows to describe deviations from the ideal flow

## Slide 5: USD Centrifugation: Shear
Pilot-Scale Disk-Stack Centrifuge
Capillary Shear Device
Rotating Shear Device
Mollet et al., 2006
Westoby et al, 2011
Levy et al., 1999, Boychyn et al., 2000
Hutchinson et al., 2006
Tait et al., 2009

## Slide 6: USD Centrifugation: RSD (Rotating Shear Device)
Difficult to directly quantify the shear rate within a centrifuge
  Limited CFD work has been published for some centrifuge models
  Easier to quantify the shear in a simplified system to estimate the energy dissipation rate indirectly
UCL developed the RDS as a way to mimic cell shear in a continuous centrifuge
Device is capable of generating different shear environments by changing the RPM

## Slide 7: USD Centrifugation: EDR (Energy Dissipation Rate)
CFD model developed to calculate the EDR within the rotating shear device
EDR values are within the range reported in literature for a pilot-scale centrifuge
Boychyn et al., (2004) Bioprocess Biosyst Eng., 26: 385–391

## Slide 8: Capillary Shear Device (CSD) Schematic Version-1
RSD is limited to 20mL per batch
>1L is typically required to perform a filter sizing study
CSD was explored to generate enough material for filter sizing studies
Syringe pump is used to control flow rate through the capillary
Pump can be programmed

## Slide 9: CSD Schematic Version-2
Version-2 utilizes an AKTA explorer piston pump and Super Loop combination as the delivery system
Able to generate high flow rates under high back pressures
  (Max = 4Mpa)
AKTA Explorer records back pressure readings and hence can be used to calculate Max EDRs

## Slide 10: Bridging Study: RDSD vs CSD
Developed capillary shear device creates the levels of shear quoted in literature to match centrifuges
  (1) Boychyn et al., (2004) Bioprocess Biosyst Eng., 26: 385–391
  (2) Westoby et al., (2011) Biotechnology and BioEngineering., 108: 990–998
Chart: 
| 12 | 14 | 16 | 18 | 20
Capillary Shear Device | 4.9961 | 6.7623 | 9.4861 | 14.6654 | 18.0673
Rotating Disk Shear Device | 9.2622 | 22.626 | 18.3785 | 15.7322
(1)
(2)

## Slide 11: USD Centrifugation Development

## Slide 12: Experimental Methodology
LDH screen
V/tΣ
screen
Verify
Scale up
Filter
Shear rates are tested to match the LDH levels found in the centrate
Range of V/tΣ values are tested to match LAPX-404 centrate
Correction factor quantified
Verification based on:
  - Turbidity
  - PSD
≈1L of USD centrate generated for filter sizing studies
Filter sizing studies conducted comparing filterability of pilot-scale and USD centrates

## Slide 13: LDH Screen
Experimentally determined EDRs suggest EDR of 2.3X105(W/Kg)
Literature values ≈ 1X105(W/Kg) quoted by:
3X104(W/Kg) Westoby et al.,(2011)
2X105(W/Kg) Boychen et al.,(2004)
Chart: Energy Dissipation Rate X105 (W/Kg)
| 0 | 0.44943820224719094 | 0.73779845505617969 | 1.232882724719101 | 1.7977528089887638 | 3.7960849719101115 | 6.1113061797752799 | 9.3556882022471886 | 13.906249999999998
 | 0 | 1.3982 | 5.0498 | 6.5848 | 11.5662 | 31.4362 | 41.0355
Pred Cent EDR | 4.8916
LDH
Screen
V/tΣ
Screen
Verify
Scale
up
Filtration
Sheared Cell Culture
 LAPX-404 Centrate

## Slide 14: Correction Factor
Correction factor identified experimentally at 0.31
Experimental value similar to those in literature of around 0.40 Pinhiero et al., (1993)
Chart: 
| 0.29400196209651064 | 0.34035300342775221 | 0.40215827720538999 | 0.48872609219948454 | 0.61871542185855222 | 0.83581538905843034
Turbidity (NTU) | 105 | 103 | 97.2 | 89.4 | 87.6 | 76
Pred Cent Correction Factor c | 105
LDH
Screen
V/tΣ
Screen
Verify
Scale
up
Filtration
Lab-scale Centrate
 LAPX-404 Centrate

## Slide 15: Verification: Turbidity
Similar turbidities were created by USD mimic to that of the LAPX-404 centrate over 10 runs
Tested multiple cell cultures
LDH
Screen
V/tΣ
Screen
Verification
Scale
up
Filtration
Chart: Lot Number
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Pilot Scale | 105 | 88 | 318 | 67.1 | 90.9 | 155 | 44 | 70 | 105 | 66.8
USD Predicted | 103 | 36 | 378 | 69.4 | 92 | 160 | 62 | 67.5 | 77 | 87.4

## Slide 16: Verification: PSD
Malvern Zetasizer used to measure PSD
Mimic centrate matched clarified material from LAPX-404 & BTPX-305
LDH
Screen
V/tΣ
Screen
Verification
Scale
up
Filtration

## Slide 17: Filterability: X0HC
Mimic material () and pilot-scale centrate () passed through 23cm2 bench-scale X0HC filter
Similar fouling observed between both during filtration
  Pressure & Turbidity
LDH
Screen
V/tΣ
Screen
Verification
Scale
up
Filtration

## Slide 18: Integrated Non Viable Cell Density (INVCD)
Integrated viable cell density (IVCD) calculated using VCD and culture time
INVCD can be used as a measure of particulates that are difficult to remove through centrifugation

## Slide 19: USD Centrifugation Predictive Data: Project A
3L Bioreactors used to generate material for experiments
Material passed through the CSD and lab-scale centrifuge to mimic LAPX-404 platform operating conditions
USD approach provided predictive capability for pilot scale performance
 LAPX-404 Centrate
 3L Model Centrate

## Slide 20: USD Centrifugation Predictive Data: Project B
INVCD used to predict performance of Project B with modelling data providing a strong fit (R2=0.98)
Strong predictive capabilities using this method.
Chart: Intergrated Non Viable Cell Density X10^5 (cell/L.hr)
| 3044.8135299999994 | 3308.1332349999998 | 3103.4960299999998 | 2844.0802299999996
A5948 3L Scale | 113 | 159 | 122 | 60.7
A5522-BB3-Pilot Scale | 116
LAPX-404 Centrate
 3L Model Centrate

## Slide 21: Conclusions USD Centrifugation
Paper accepted by Journal of Biotechnology & Bioengineering
The scale-down model generated comparable material on multiple occasions:
  Confirmed similar shear rate by matching increase in LDH
  Settling characteristics confirmed by turbidity
  Particle size distribution profiles are similar
  Matching filtration pressure and turbidity profiles
Significant savings in Material, Cost & Time:
50L Stainless Steel → 3L Bench Reactor
Allows for centrifuge characterization at an earlier stage of process development
Plan to extend work to include samples from a commercial scale centrifuge

## Slide 22: Depth Filtration Development Strategy

## Slide 23: Introduction
Depth filters are used in combination with a disk-stack centrifuge or as a train.
  Characterization requires large material & resource requirement
  Sizing only conducted for worse case material
Development of more efficient method for filter sizing
Two main modes of filtration
Constant Flow Constant Pressure
  Experimentally determined capacity Theoretically determined capacity
  Used to size depth filters Used to size Sterile Filters
  Requires large pools of material (1.5 L) Requires small pool of material
Developed method benefits
  Material & time reduction for characterization
  Wider range of materials tested
Established predictive models for D0HC and X0HC filters
Constant Flow
Constant Pressure

## Slide 24: Constant Flow Constant Pressure
A
B

## Slide 25: D0HC Prediction Strategy
Requirements of good correlation between CFcap and Ks
Also accurate quantification of Ks

## Slide 26: Fouling Analysis
Chart: V
| 100 | 200 | 300 | 400

Chart: V
| 100 | 200 | 300 | 400

Chart: V
| 100 | 200 | 300 | 400

Chart: t
| 100 | 200 | 300 | 400

Constant pressure experiments data analyzed to identify best model by linearity (R2)
Data analyzed to quantify gradient for each data set (Ki)
Complete
Cake
Intermediate
Standard
K1(R2)
K2(R2)
K3(R2)
Scaling and Particulate Fouling in Membrane Filtration Systems Volume 26 of IHE Dissertation Page 123

## Slide 27: D0HC Constant Pressure Fitting Data
Blocking | Complete | Cake | Intermediate | Standard
Figure |  |  |  | 
Model |  |  |  | 
Fit to CP Data (R2) | 0.86 | 0.82 | 0.74 | 0.99
Fit to CF Predictions (R2) | 0.61 | 0.38 | 0.52 | 0.92
Blocking | Complete | Cake | Intermediate | Standard
Figure |  |  |  | 
Model |  |  |  | 
Fit to CP Data (R2) | 0.86 | 0.82 | 0.74 | 0.99
Fit to CF Predictions (R2) | 0.61 | 0.38 | 0.52 | 0.92
4 standard fouling mechanisms when operating at constant pressure
  Other combination models can also be used to describe the fouling

## Slide 28: D0HC Filtration Capacity Prediction
10 separate cell cultures sourced from 3 projects were used during the development of this model.
Strong correlation between CP fouling coefficient and CF capacity R2=0.92
Independent verification run to confirm findings
Chart: Constant Pressure Fouling Coefficient (KS)
| 1.0924312E-2 | 1.4084012E-2 | 1.2828763999999999E-2 | 1.3515008E-2 | 8.0971849999999998E-3 | 4.2667310000000002E-3 | 5.4384159999999997E-3 | 9.5739829999999995E-3 | 4.4453690000000002E-3 | 5.7099430000000003E-3
 | 58.2895 | 39.04 | 42.5988 | 49.0967 | 116.6986 | 142.932 | 105.387 | 92.0882 | 126.3748 | 124.2794

## Slide 29: D0HC Model Verification
Average deviation between experimental and predicted value is 14.4%
Filter to filter deviation is around 30%** for Millipore depth filters.
**The clarification of bioreactor cell cultures for biopharmaceuticals Yavorsky et al., (2003) Pharm Technol
Chart: Constant Flow Capacity (L/m2)
| Lot-A | Lot-B | Lot-C
CF Experimental Capacity (30 LMH) | 107.8325 | 105.1397 | 104.208
CP Predicted Capacity (10psi) | 89.5684 | 90.8855 | 89.9836

## Slide 30: X0HC Model Verification
Cake Model
  Fit to CP Data: R2=0.85
  Fit to CF Predictions: R2 =0.90
Cake Adsorption Model
  Fit to CP Data: R2 =0.93
  Fit to CF Predictions: R2 =0.95
Independent material tested to verify the modelling data set
Strong predictions for both Standard and Mixed models

## Slide 31: Conclusion Scale-Down Depth Filtration
Novel method of sizing depth filters
Paper submitted to Journal of Membrane Sciences
The newly developed approach requires:
1-2L Centrate /Cell Culture → 100mL Centrate /Cell Culture
5 Hrs Process Time → 3 mins Process Time
Constant flow capacity predicted using constant pressure data within ±15% for both X0HC and D0HC filters
Potential for method to be used for screening at an earlier stage of process development

## Slide 32: Acknowledgements
J.Bender
S.Bosley & M.Meyers
J.Dyer II
S.Goldrick, D.Gruber & R.Turner
K.Hwang
N.Fuchs, M.Liang, A.Martinez, K.Singarapu & W.Yang
B.Kenty
Proff. N.Titchener-Hooker & Proff. SS.Farid
M.Mollet
M.Mlawa
S.Rose
J.Savery
Franklin Building
OMW
UCL