## Slide 1: Figures and tables for (high level) Common Framework article

## Slide 2: Table 1: Integrated and Continuous Bioprocessing Implementation
 | N-1 | N Brx | Number of Columns | Virus inact. | Number of Columns | Number of Columns | Virus Filter | UFDF | GMP?
Amgen | ? | Perf | Single | Batch | Single | Single | Batch | Batch | Y
AstraZeneca | Perf | Perf | Multi | TBD | Single | Single | Batch | Batch | N
Bayer | ? | Batch | Multi | Cont. | Multi | Multi | ? | ? | ?
Biosana | ? | Perf | Multi | Batch | Multi | Multi | Cont. | Batch | Y
BMS | Perf | Batch | Multi | Batch | Single | Single | Batch | Batch | Y
Janssen | Perf | Batch | Single | Batch | Single | Single | Batch | Batch | Y
Just | Perf | Perf | Multi | Batch | Multi | Multi | Cont. | Cont. | Y
Lilly | Batch | Batch | Single | Batch | Single | Single | Batch | Batch | Y
Merck (KgaA) | ? | Batch | Multi | Cont. | Multi | Multi | Batch | Batch | Y
Merck (MSD) | Perf | Perf | Multi | Batch | Multi | Multi | Cont. | Batch | Y
Novartis | Perf | Perf | Multi | Batch | Single | Single | Cont. | Cont. | Y
Pfizer/BI | Perf | Perf | Multi | Cont. | Single | Single | Batch | Batch | N
Sanofi | TBD | Perf | Multi | Both | Multi | Multi | Cont. | Cont. | Y
WuXi | Perf | Perf | Multi | ? | Multi | Multi | ? | ? | ?

## Slide 3: Figure 1: Common Framework for Integrated and Continuous Processing
??
??
SPTFF or
UF/DF
Capture
Polishing
Polishing
VRF
N-stage Bioreactors
120-500kg
Virus Inactivation
Feeds
N-1
ATF
In-line titration
Tank or PFR
In-line titration
In-line titration
Cell Retention
Surge tank
Surge tank
Optional lot pool
Will be more professionally drawn

## Slide 4: Table 2: Bioreactor Assumptions
N-stage bioreactor Size (L) | 500-2000
Number of bioreactors | 1-4
Avg cell density (million cells/mL) | 50-120
Qp (pg/cell/day) | 20-40
Permeate Perfusion Rate (bioreactor volumes/day, vvd) | 0.5-2 (1.5)
Lot (Batch) Duration (days) | 20
Number of concentrated media feeds | 1-5 (3)
Media Concentration Factor | 1x to 5x (20x, 12x, and 5x)
Range of parameters (parenthetical values used in examples)

## Slide 5: Table 2: Productivity, capacity, yield, and solution use
*The number of buffers does not include the VI/VRF buffers, as those will not go into large buffer tanks. The sanitization solution is assumed to be common among all steps.
400kg buffer/kg BDS equally divided among 14 buffers means each kg of BDS requires 29L of each buffer.
Bioreactor yield includes 90% yield of cell retention step
PMI: Product Mass Index; ILC: In-line conditioning; DF: diafiltration
 | Productivity/ Capacity/ Diafiltration Product Concentration | Volume Used (L/L) (Perfusion, Wash, diafiltration volume) | Yield | Number of Solutions per Step | PMI (L/kg) | Concentrate Factor | PMI for Concentrates | ILC Concentration Factor | PMI for ILC
Bioreactor | 4.8 | 1.5 | 100% | 3 | 529 | 3 | 176 |  | 
TFF | 1000L/m2 | NA | 90% | NA | NA | NA | NA |  | 
ProA | 60 | 21 | 90% | 7 | 534 | 5 | 107 | 20 | 26.7
VI | NA | 0.1 | 100% | NA | 15 | 1 | 15 | 1 | 15.0
AEX | 100 | 16 | 95% | 4 | 220 | 5 | 44 | 20 | 11.0
CEX | 40 | 16 | 85% | 5 | 521 | 5 | 104 | 20 | 26.1
VRF | 700g/m2 | NA | 95% | NA | 15 | 5 | 3 | 5 | 3.0
UFDF | 50 | 6 | 95% | 2 | 126 | 1 | 126 | 20 | 6.3
Overall |  |  | 59% | 14 | 1960 |  | 576 |  | 88

## Slide 6: Figure 2
Will be more professionally drawn

## Slide 7: Figure 5A: Batch-wise UFDF
Conc 1 tank
Small UF for end-to-end daily concentration
DF tank
Lot Pool Tank
DF solution
Product Stream
Will be more professionally drawn

## Slide 8: Figure 5B: Single-Pass Tangential Flow Filtration and In-Line Diafiltration
Single pass concentration
Multi-stage in-line diafiltration
Single pass final concentration
Will be more professionally drawn